| Form 90 Revised: Feb. 14 | Culvert Rating Form |
| --- | --- |

| Bridge Number: | Year Built: | Year Remodeled: |
| --- | --- | --- |
| County: | Bridge Owner: |
| Route: | Feature Crossed: |
| Culvert Type: |
| Structure Type Code: | Culvert Dimensions: |
| No. of Barrels: | Barrel Length: |
| Rating Guidelines |
| Material | Culvert Type | Structure Type Code | Inventory Load Rating | Operating Load Rating |
| Cast- in-place Concrete | Box | 113 | HS 22.0 | HS 33.0 |
|  | Type W Box (1930 era) | 113 | HS 16.0 | HS 24.0 |
|  | Footing Supported Arch | 112 | HS 20.0 | HS 30.0 |
| Precast Concrete | Box (prior to 1989) | 513 | HS 24.0 | HS 36.0 |
|  | Box (1989 – 2010) * | 513 | HS 25.0 | HS 42.0 |
|  | Box (2011 & after) ** | 513 | RF=1.0 | RF=1.3 |
|  | Footing Supported Arch | 512 | HS 20.0 | HS 30.0 |
|  | Round Pipe | 514 | HS 24.0 | HS 36.0 |
|  | Pipe-Arch | 515 | HS 22.0 | HS 33.0 |
| Aluminum | Box | 913 | HS 14.0 | HS 21.0 |
| Metal | Footing Supported Arch | 312 | HS 12.0 | HS 18.0 |
|  | Round Pipe | 314 | HS 16.0 | HS 24.0 |
|  | Pipe-Arch | 315 | HS 16.0 | HS 24.0 |
|  | Elliptical | 316 | HS 16.0 | HS 24.0 |
| Timber | Box | 713 | HS 14.0 | HS 21.0 |
| Masonry | Footing Supported Arch | 812 | HS 18.0 | HS 27.0 |
| ( Structures with Load Factor HS 25 Design |
| (( Structures with LRFD HL 93 Design using Standard Plans – Precast Concrete Box Culvert |

The above table may be used as a guideline to the culvert rating.

| Inventory Rating |  |  | Operating Rating |  |
| --- | --- | --- | --- | --- |

NBI Condition Rating: Culvert _______ If the culvert condition rating is 4 or less, do not use this form. Instead, rate by Physical Inspection Rating (Form_PIR).

(Typed or Printed) Name: 		Date:

(Typed or Printed) Title:

(Typed or Printed) Employed by (Agency / Firm):